## Slide 1
UNIVERSITY OF DODOMA | CT321 | 2025/2026
Analog Temperature
Monitoring System
Using ATmega32 ADC, LM35 Sensor
KiCad · SimulIDE · MPLAB for VS Code
PBL Project 2 – Group 2
Notes: Welcome everyone. This is Group 1's presentation for CG 221 PBL Project 2. We built a complete Analog Temperature Monitoring System using the ATmega32 microcontroller.

## Slide 2
Presentation Outline
01
Introduction & Problem Statement
02
System Block Diagram
03
ATmega32 Pin Mapping
04
Firmware Design & Flowchart
05
KiCad Schematic & PCB
06
SimulIDE Simulation & Results
07
ADC Calculations
08
GitHub Repository & Conclusion
Notes: Here is a quick overview of what we will cover today.

## Slide 3
Introduction
& Problem Statement
ADC
Analog-to-Digital
Converter
LM35
Precision Temp
Sensor
AVR
ATmega32
8-bit MCU
Background
Real-world signals (temperature, pressure, sound) are analog. The ATmega32 is a purely digital device — it cannot process these signals directly.
An ADC is required to bridge the gap, converting a continuously varying analog voltage into discrete digital values the microcontroller can act upon.
Problem Statement
Industries — agriculture, healthcare, data centers, manufacturing — need continuous temperature monitoring. This project implements a standalone MCU-based system that:
• Reads temperature from an analog sensor
• Classifies readings into Low / Normal / High
• Provides visual LED and audio buzzer alerts
• Optionally logs data via USART serial output
Since physical hardware is unavailable, demonstration is done via SimulIDE simulation.
Notes: The ATmega32 is an 8-bit AVR microcontroller. It can only process digital signals, so we use its built-in 10-bit ADC to read the analog voltage from the LM35 sensor.

## Slide 4
Project Objectives
1
Configure ATmega32 ADC
Set up 10-bit ADC on channel ADC0 (PA0) using ADMUX & ADCSRA registers
2
Interface LM35 Sensor
Connect precision analog temp sensor outputting 10 mV per °C
3
ADC → Temperature
Convert digital ADC counts to °C using integer arithmetic formula
4
3-State Classification
Classify into Low (<25°C), Normal (25–35°C), and High (>35°C)
5
LED & Buzzer Outputs
Drive Green, Yellow, Red LEDs and buzzer based on temperature zone
6
USART Data Logging
Transmit formatted temperature strings to PC terminal at 9600 bps
7
KiCad Design
Design full schematic and PCB layout with ERC/DRC passing
8
SimulIDE Simulation
Build and validate all conditions without physical hardware
Notes: We had 8 clear objectives for this project covering hardware, firmware, simulation, and documentation.

## Slide 5
System Block Diagram
LM35
Sensor
Analog Input
ATmega32
ADC (PA0)
10-bit Digitizer
ATmega32
CPU
Firmware Logic
Green LED (PB0)
Low Temp <25°C
Yellow LED (PB1)
Normal 25–35°C
Red LED (PB3)
High Temp >35°C
Buzzer PB6
Analog Voltage (10 mV/°C)
Digital (0–1023)
Notes: The LM35 outputs 10 millivolts per degree Celsius. This analog voltage goes into the ATmega32 ADC on pin PA0. The firmware processes it and drives the output peripherals.

## Slide 6
ATmega32 Pin Mapping
PA0 / ADC0
Input (Analog) · ADC Channel 0
LM35 Output
PB0
Output · LED – Low Temp
Green/Blue LED
PB1
Output · LED – Normal
Yellow LED
PB2
Output · LED – High
Red LED
PB3
Output · Buzzer Drive
Buzzer (2N2222)
AVCC / AREF
Power/Ref · ADC Supply + Ref
100 nF caps
XTAL1/2
Clock · 16 MHz Crystal
Y1 + 22 pF caps
Notes: PA0 is used as the analog input. Port B pins 0-3 drive the LEDs and buzzer. PD1 handles USART transmit. AVCC and AREF need proper decoupling capacitors for clean ADC readings.

## Slide 7
Firmware Design & Flowchart
START
Initialize I/O, ADC, USART
Start ADC Conversion (ADSC=1)
Wait for ADSC to clear
Read ADC Result (10-bit)
Convert: Temp = ADC×500/1023
Classify: Low / Normal / High
Drive LED + Buzzer outputs
LOOP
loop
Firmware Highlights
Language:
C (ANSI C99) – XC8 / avr-gcc
ADC Setup:
ADMUX = 0x40 (AVCC ref, CH0)
ADCSRA = 0x87 (EN + prescaler /128)
Temp Formula:
T°C = (ADC × 500) / 1023
Integer math — no float!
Error Check:
ADC < 5 or > 900 → blink all LEDs
+ send error via USART
Loop Delay:
500 ms between samples
(_delay_ms from <util/delay.h>)
Notes: The firmware uses only integer arithmetic to avoid floating-point overhead on the 8-bit AVR. The formula T = ADC×500/1023 is accurate to within half a degree Celsius.

## Slide 8
KiCad Schematic & PCB Design
Schematic Design
· ATmega32-16PU as main MCU
· LM35DZ sensor → PA0 via 100 nF filter
· 3× LEDs with 330 Ω current-limiting resistors
· Buzzer driven by 2N2222 NPN transistor
· 1N4148 flyback diode across buzzer
· 10 kΩ pull-up reset button circuit
· 16 MHz crystal + 22 pF load capacitors
· 100 nF decoupling caps on VCC, AVCC, AREF
· USART 6-pin header connector
· ERC: 0 Errors, 0 Warnings ✓
PCB Layout
Board Size:
~80 × 60 mm compact layout
LM35 Placement:
Board edge — away from heat sources
ADC Trace:
Short, direct to PA0 — away from digital traces
Decoupling Caps:
C3 & C4 within 2 mm of MCU pins
Ground Plane:
Solid GND pour on back copper layer
Power Traces:
VCC/GND ≥ 0.5 mm wide
Silkscreen:
All refs labeled: U1, U2, D1–D4, R1–R5…
DRC:
0 Errors, 0 Warnings ✓
Gerber Files Generated: F_Cu · B_Cu · F_SilkS · F_Mask · B_Mask · Edge_Cuts · .drl
Notes: The schematic was drawn in KiCad 7. The PCB was carefully laid out with the LM35 at the board edge for good airflow, and decoupling capacitors placed as close as possible to the MCU pins.

## Slide 12
SimulIDE Simulation Results
LM35 model not available in SimulIDE — potentiometer used to simulate equivalent sensor voltage
TC-01
Low Temperature
Input:
~0.20 V
ADC Count:
~41
Temp:
~20°C
LED:
Green/Blue LED ON
Buzzer:
Buzzer OFF
✓ PASS
TC-02
Normal Temperature
Input:
~0.30 V
ADC Count:
~61
Temp:
~30°C
LED:
Yellow LED ON
Buzzer:
Buzzer OFF
✓ PASS
TC-03
High Temperature
Input:
~0.40 V
ADC Count:
~82
Temp:
~40°C
LED:
Red LED ON
Buzzer:
Buzzer ON
✓ PASS
TC-04
Sensor Error
Input:
~0 V
ADC Count:
<5
Temp:
N/A
LED:
All LEDs blink
Buzzer:
Error via USART
✓ PASS
All 8 test cases passed — including boundary tests at 25°C and 35°C, dynamic transitions, and USART serial output
Notes: We tested four main conditions plus boundary tests. The ADC reads correctly and the firmware correctly switches between LED states. USART output was confirmed in SimulIDE's serial monitor.

## Slide 13
ADC Calculations
Key Formulas
ADC Resolution:
5.0 V ÷ 1023 ≈ 4.887 mV / LSB
ADC from Voltage:
ADC = (Vin × 1023) / 5.0
Voltage from ADC:
Vin = (ADC × 5.0) / 1023
Temp from Voltage:
T°C = Vin / 0.010 (LM35: 10 mV/°C)
Combined Formula:
T°C = (ADC × 500) / 1023
Worked Example – 30°C
Step 1: V_in = 30°C × 10 mV/°C = 300 mV = 0.300 V
Step 2: ADC = (0.300 × 1023) / 5.0 ≈ 61 counts
Step 3: T = (61 × 500) / 1023 = 30500 / 1023 ≈ 29.8°C ✓
Conversion Table
Temp (°C)
LM35 (mV)
ADC Count
Firmware °C
0°C
0 mV
0
0°C
20°C
200 mV
41
20°C
25°C
250 mV
51
25°C
30°C
300 mV
61
30°C
35°C
350 mV
72
35°C
40°C
400 mV
82
40°C
50°C
500 mV
102
50°C
100°C
1000 mV
205
100°C
Notes: The integer formula T = ADC×500/1023 is accurate to within half a degree Celsius, which matches the LM35 sensor's own typical accuracy of plus or minus half a degree.

## Slide 14
Complete Test Results
Chart: ADC Counts by Test Case
| TC-01 20°C | TC-02 30°C | TC-03 40°C | TC-05 25°C | TC-06 35°C | TC-07 20→40°C
ADC Count | 41 | 61 | 82 | 51 | 72 | 62
All 8 Test Cases
TC-01
Low Temp
✓
TC-02
Normal Temp
✓
TC-03
High Temp
✓
TC-04
Sensor Error
✓
TC-05
Boundary 25°C
✓
TC-06
Boundary 35°C
✓
TC-07
Dynamic Low→High
✓
TC-08
USART Output
✓
8/8
Test Cases
Passed
100%
Pass
Rate
±0.5°C
Calculation
Accuracy
Notes: All eight test cases passed in SimulIDE. The firmware correctly handles all temperature zones, boundary conditions, sensor errors, and USART data logging.

## Slide 15
GitHub Repository
ATmega32_ADC_Temperature_Monitor
Visibility:
Public · MIT License
Commits:
11 structured commits
URL:
https://github.com/panthermodes/ANALOGY-TEMPERATURE-MONITORING-SYSTEM-GROUP2.git
Repository Structure
📁 firmware / src / main.c · hex / *.hex
📁 kicad / schematic / · pcb / · gerber /
📁 simulide / circuit / · screenshots /
📁 documentation / block_diagram · flowchart
📄 README.md (project overview + setup)
📁 media / demonstration_video_link.txt
Commit History
#1 – Initial repo + README
#2 – Firmware: main.c + config.h
#3 – KiCad schematic
#4 – PCB layout + 3D screenshots
#5 – Gerber manufacturing files
#6 – Compiled HEX file
#7 – SimulIDE circuit + test screenshots
#8 – ADC calculation documentation
#9 – Pin mapping + test results
#10 – Block diagram + flowchart
#11 – Demonstration video link
Notes: The repository has 11 commits following good version control practices — each commit covers one logical milestone of the project.

## Slide 16
Conclusion
10/10
Tasks Completed
8/8
Test Cases Passed
11
Git Commits
7
Gerber Layers
Key Learning Outcomes
✓ ATmega32 ADC configuration using ADMUX & ADCSRA registers
✓ Analog sensor interfacing — LM35 precision temperature sensor
✓ Integer-based ADC-to-temperature conversion (no floating point overhead)
✓ GPIO output control for LEDs and buzzer via DDRB & PORTB registers
✓ USART initialization and character transmission for serial data logging
✓ KiCad schematic & PCB design including analog signal routing best practices
✓ SimulIDE circuit simulation for firmware validation without physical hardware
✓ Professional documentation and GitHub version control practices
University of Dodoma (CIVE) · CG 221 · Group 2 · 2025/2026
Notes: In conclusion, we successfully built a complete temperature monitoring system from schematic design to simulation. The project gave us hands-on experience with AVR microcontroller programming, analog sensor interfacing, PCB design, and proper documentation practices. Thank you.